## Slide 1: Basic Sensors
ENGG 6150: Bio-Instrumentation

## Slide 2: Basic Sensors
Displacement Measurement Resistive Sensors
  Whetstone Bridge Circuits
  Inductive Sensors
  Capacitive Sensors
  Piezoelectric Sensors
Temperature Measurement
  Temperature Sensors
Optical Measurements
  Light Sensors
Solid-State Sensors
MEMS Sensors
Sensor Calibration

## Slide 3: Transducers
  Transducer
    a device that converts a primary form of energy into a corresponding signal with a different energy form
      Primary Energy Forms: mechanical, thermal, electromagnetic, optical, chemical, etc.
    take form of a sensor or an actuator
  Sensor (e.g., thermometer)
    a device that detects/measures a signal or stimulus
    acquires information from the “real world”
  Actuator (e.g., heater)
    a device that generates a signal or stimulus

## Slide 4: Sensor Systems
Typically we are interested in electronic sensor
Typical Electronic Sensor “System” consist of two transducers:
The primary converts the measured phenimna from one
Physical domain into another
The secondary part converts the recent physical domain into electrically measurable signal

## Slide 5: Typical Instrumentation
Sensor/sensors are the interface to the measurand
Data is obtained from the output of the sensors to be conditioned before processing
Data is stored and analyzed by personnel in control

## Slide 6: Electrical Circuits Definitions and Analyses
Since the signal we are processing as an output from the sensor/transducers is an electrical signal then we need to cover the below definitions and some circuit analyses
  Current and its relation to charge, i.e. integration and derivation
  Ohm’s Law
  Power
  Energy
  Passive components including wires, resistors, capacitors and inductors
  Voltage and current sources

## Slide 7
Basic Quantities
Electrical current:
Flow of electrons through a wire or other
electrical conductor
Electrons are negatively charged particles
- The time rate of flow of electrical charge
through a conductor or circuit element
- The units are amperes (A), which are
equivalent to coulombs per second (C/s)
- The charge per electron is -1.602×10-19 C

## Slide 8
- If the charge is given determine the current by
Differentiation
- If the current is known determine the charge by
Integration
A physical analogy that helps visualize electric
Currents is that of water flow.
Charges are visualized as water particles

## Slide 9
Voltage:
- The force that pushes electricity through a wire
- The voltage associated with a circuit element
is the energy transferred per unit of charge
that flows through the element. The units of
voltage are volts (V), which are equivalent to
joules per coulomb (J/C)

## Slide 12
A consequence of this convention is that the reference directions for current and voltage are not independent

## Slide 15
P1 = 12W
P2 = 36W
P3 = -48W
IMPORTANT: NOTICE THE POWER BALANCE IN THE CIRCUIT
COMPUTE POWER ABSORBED OR SUPPLIED BY EACH ELEMENT
Example

## Slide 19: Why using Kirchhoff’s Laws??
When the circuit has components of resistors that are neither in series nor in parallel then Ohm’s law is not enough to find the currents and voltages.
For those complex circuits we need to use more advanced techniques such as Kirchhoff’s current and voltage laws.

## Slide 20
Circuit Definitions
  Wires - are assumed to have negligible resistance
  Node/junction/net
  Branches
Loop

## Slide 21: Node/Junction/Net
A node/junction/net – any point on a wire or web of wires where 2 or more circuit elements are connected together via
  Each node/junction/net has one voltage (w.r.t. ground)
In the circuit shown below we have three nodes/junctions/nets

## Slide 22: Node/Junction/Net
Circuits (a) and (b) are identical electrically, however, when it comes to drawing the circuit using dedicated schematic software then circuit (a) is the professional circuit schematic to do and use. It “looks neater”
(a)
(b)

## Slide 23: Branches
A branch – a circuit element that is between two nodes/junctions/nets
In the following circuit, there are five branches in the circuit bellow as:

## Slide 24
Kirchhoff’s Current Law (KCL)
  KCL states: The net current entering a node is zero.
  Mathematically
  Based upon conservation of charge – the algebraic sum of the charge within a system can not change.
  A Node connects several components however it does not hold any charge. i.e., no charges are accumulated at a node

## Slide 25: Kirchhoff’s Current Law (KCL)
i1
i3
i2
i3
i4
You can assume that
Entering currents are +ve currents
Leaving currents are -ve currents
Or
Leaving currents are +ve currents
Entering currents are -ve currents
But for the same circuit you MUST stick to ONE convention

## Slide 26: Kirchhoff’s Current Law (KCL) Example 1
Using KCL, determine I, the current flowing out of the voltage source.
Based on the assumption that states:
1- Leaving currents are +ve currents
2- Entering currents are -ve currents
We can write the following equation:
  -1.9 mA - 0.5 mA + 3mA - I =0
  I = 0.6 mA
  Note that V1 is supplying power.

## Slide 27: Kirchhoff’s Current Law (KCL) Example 2
Suppose the current through R2 was entering the node and the current through R3 was leaving the node.
  The KCL equation using the previous assumption is:
  -3 mA +1.9 mA - 0.5 mA - I =0
  I = -1.6 mA
  Note that V1 is absorbing power.

## Slide 28: Equivalent Current Source using KCL
Applying KCL at node a yield:

## Slide 29
Exercises

## Slide 30: Kirchhoff’s Voltage Loop (KVL)
A loop is: a collection of branches that form a closed path returning to the same node/junction/net without going through any other nodes or branches twice
KVL states: the algebraic sum of the voltages equals zero for any closed path (loop) in an electrical circuit
Mathematically is:
We have two conventions to pick from when writing a KVL equation. The adopted convention should be the same for all voltages in one loop. Those conventions are “potential gains” or “potential losses”

## Slide 31: Writing KVL Equation using “Potential Gains” Convention
By using this convention, voltage drop is written as positive when moving from the negative terminal to the positive terminal of the element
In other words if the direction of the loop
agrees with the current direction
for the resistor then it is written as negative
P.S. For voltage sources if the direction of the
loop enters the negative terminal then the
voltage is written as positive

## Slide 32: Writing KVL Equation using “Potential Losses” Convention
By using this convention, voltage drop is written as positive when moving from the positive terminal to the negative terminal of the element
In other words if the direction of the loop
agrees with the current direction
for the resistor then it is written as positive
P.S. For voltage sources if the direction of the
loop enters the negative terminal then the
voltage is written as negative

## Slide 33: Writing KVL Equations
Write all KVL equations for the circuit below adopting one of the conventions. Using “Potential Losses” yields:
I1
I3
I2
R1
Vs1
R2
Vs2
A
C
B
D
Vs3
E
L2
L1
L3
R3
Step1, distribute currents on all branches the way you desire
Step2, draw the KVL loops the direction you desire
Step3, write the KVL equations such that loop direction agreeing with current direction is written as +RI and loop direction entering negative voltage source is written as
KVL@
KVL@
KVL@
Notes: Potential loss as positive means that voltage is positive when it flows from positive to negative;
L1: -Vs1 + I1R1 + Vs3 –I3R3 = 0 ; L2: -Vs1 + I1R1 +I2R2+Vs2 = 0; L3: -Vs2 - I2R2 + Vs3 –I3R3 = 0
Potential gain as positive means that voltage is positive when it flows from negative to positive.

## Slide 34: Writing KVL Equations
Write all KVL equations for the circuit below adopting one of the conventions. Using “Potential Gains” yields:
I1
I3
I2
R1
Vs1
R2
Vs2
A
C
B
D
Vs3
E
L2
L1
L3
R3
Step1, distribute currents on all branches the way you desire
Step2, draw the KVL loops the direction you desire
Step3, write the KVL equations such that loop direction agreeing with current direction is written as -RI and loop direction entering negative voltage source is written as
KVL@
KVL@
KVL@

## Slide 35: Writing KVL Equations using Double Indices Notation
The loop does not have to be a physical loop however it has to belong to the same circuit
+
-
The means that the potential at b is greater than the potential at e .i.e., is positive.
In order to calculate assuming are known, we can write the KVL equation using the “potential losses” convention as follow:
KVL@

## Slide 36: The Number of Independent KCL & KVL Equations
N is the number of nodes, here N = 5
The number of independent KCL equations
are N-1 = 4. However, since is the
same in is the same in
, and is the same in
we end up with one useful
KCL equation as follow:
KCL@B :
The independent KVL equations are
B-(N-1) where B is the number of
branches between the identified number of nodes
B=6 and B-(N-1) = 6-4=2
KVL@
KVL@
I1
I3
I2
R1
Vs1
R2
Vs2
A
C
B
D
Vs3
E
L2
L1
L3
R3
Using “Potential Losses” convention

## Slide 37
Dependent Sources are handled with the same ease
KVL Examples

## Slide 38: Equivalent Voltage Source using KVL
Applying KVL on circuit (a) using
“Potential Losses” convention yields:
Note: To avoid violating KVL, a
circuit can not contain two parallel
voltage sources that are not equal

## Slide 39: All Rules in one Example
a
b
c
d
e
+
-
+
-
+
-
+ -
+
-
Identify distinguished nodes
Given sing KVL and KCL find , solution is:
Assign arbitrary currents
Using Ohm’s law
KVL@
P.S. 1- Potential Losses for KVL, and 2- entering currents are negative for KCL are adopted here.

## Slide 40
(a)
(b)
(c)
(d)
Exercises

## Slide 41: Sinusoids
A sinusoid is a signal that has the form of the sine or cosine function.
A general expression for the sinusoid,
where
Vm = the amplitude (peak) of the sinusoid
ω = the angular frequency in radians/s
Ф = the phase
T = Period

## Slide 42: Sinusoids
A periodic function is one that satisfies v(t) = v(t + nT), for all t and for all integers n where T is the period.
Only two sinusoidal values with the same frequency can be compared by their amplitude and phase difference.
If phase difference is zero, they are in phase; if phase difference is not zero, they are out of phase.

## Slide 43: Phasors
A phasor is a complex number that represents the amplitude and phase of a sinusoid.
It can be represented in one of the following forms:
Rectangular
Polar
where

## Slide 44: Phasors
Transform a sinusoid to and from the time domain to the phasor domain:
(time domain) (phasor domain)
Amplitude and phase difference are two principal concerns in the study of voltage and current sinusoids.
Phasor will be defined from the cosine function in all our proceeding study. If a voltage or current expression is in the form of a sine, it will be changed to a cosine by subtracting from the phase.

## Slide 45: Complex Numbers
To add or subtract two numbers you must convert them to rectangular first and then do the operation
To multiply two complex numbers in polar form
To divide two complex numbers in polar form

## Slide 46: Trigonometric Identities
As an example, take ) that start on the positive axis of ) then rotating + (clock wise) will give -) as a result
Cos(
Sin(
-

## Slide 47: COMPLEX IMPEDANCES: Inductances
Current through the inductor lags the voltage by 90o
ZL = jwL is called the impedance of
the inductance (measured in ohms)
Ohm’s law in phasor form
i.e., we need the positive Cos function that is equivalent to

## Slide 48
COMPLEX IMPEDANCES: Capacitance
Current through the capacitor leads the voltage by 90o

## Slide 49
COMPLEX IMPEDANCES: Resistance

## Slide 50: Phasor Relationships for Circuit Elements
Summary of voltage-current relationship |  | 
Element | Time domain | Frequency domain
R |  | 
L |  | 
C |  | 

## Slide 51: Impedance and Admittance

## Slide 52: Circuit Analysis Using Phasors and Impedances
1. Replace the time descriptions of the voltage and current sources with the corresponding phasors. (All of the sources must have the same frequency.)

## Slide 53
2. Replace inductances by their complex
impedances ZL = jωL. Replace
capacitances by their complex impedances ZC = 1/(jωC). Resistances have impedances equal to their resistances.
3. Analyze the circuit using any of the techniques studied earlier for DC circuits, performing the calculations with complex arithmetic.

## Slide 54
Example 7: Use nodal analysis to find v1(t) in steady state.
Solving (1a) and (2a)